## Slide 1
SIDAR: Open Indoor Scene Data Acquisition and Format Pipeline
A generic mobile-to-robotics toolchain for synchronized RGB-D capture, phone-side annotation, open scene packaging, validation, rendering, and ROS2 export.
On-device Capture App
iPhone ARKit/LiDAR app shown to users as SIDAR
Open Scene Package
Inspectable directory format with documented files
Workstation Processing Tools
Command-line modules for validation, conversion, rendering, and export
Standard Outputs
Reusable scene assets and robot-data products
Recorded Streams
Phone-side Functions
ARKit / LiDAR Session
tracking + depth
RGB Recorder
capturedImage
Depth and Confidence
meters and quality
Pose and Intrinsics
timestamps and K
Optional ARKit Mesh Export
world-frame PLY
Scene Gallery
browse, rename, delete
Upload
token and progress
Top-down Room Annotation
polygons and z bands
3D Preview
inspect mesh
RGB Mesh Colorization
colorized preview
Local storage
plus optional
HTTP upload
.phonescene
open capture package
metadata.json
manifest.jsonl
rgb/*.png
depth/*.f32
confidence/*.u8
mesh/arkit_mesh_world.ply
annotation/gt_rooms.json
annotation/topdown_map.png
preview_mesh*.json/bin
room GT
preview
Directory-based, inspectable, copyable, and free of custom binary dependencies
Package Intake
receiver.py: HTTP receiver, token checking, staging, package validation
SIDAR Receiver
Scene Validator
validation.py: files, depth, intrinsics, pose continuity, tracking state
Coordinate Conversion
coordinates.py: ARKit world to ROS world; camera and mesh frames
Mesh / USD Builder
mesh.py: ARKit mesh or depth triangles; scene.usda export
Isaac Render Script
isaac.py: RGB-D and pose render package from USD scene
ROS2 Bag Writer
rosbag_writer.py: MP3D-compatible topic contract; rosbag2 output
CLI Entrypoint
cli.py
phone-scene
receive | validate | build-mesh | make-isaac-script | render-to-bag
.phonescene
direct open capture package
gt_rooms.json
world polygons and z bands
scene.usd(a)
metric 3D scene asset
render package
metadata, RGB, depth, pose
ROS2 Bag Topic Contract
/tesse/left_cam/rgb/image_raw
/tesse/left_cam/camera_info
/tesse/depth_cam/mono/image_raw
/tesse/seg_cam/converted/image_raw
/tf, /tf_static
All outputs are documented and reusable beyond any particular experiment or downstream method.